## Slide 1: Filtering Noisy Audio
Signals & Systems Lab Project
Prepared By:
Ali Asghar (21PWCSE2059)
Suleman Shah (21PWCSE1983)
Shahzad Bangash (21PWCSE1980)

## Slide 2: Overview:
Introduction
Problem Statement
Project Source
Tools used in the project
Project Flow Diagram
Methodology
  Signal Analysis
  Filter Design
  Impulse Response Calculation
  Filtering process
  Results
Conclusion
References
Page #3
Page #4
Page #5
Page #6
Page #7
Page #7
Page #8
Page #11
Page #14
Page #16
Page #18
Page #19
Page #20

## Slide 3: Introduction:
The project aims to analyze and process a noisy audio signal using filtering techniques to attenuate unwanted noise and improve audio quality. It involves exploring
frequency characteristics
designing filters
analyzing their response
and evaluating filtered audio outputs.

## Slide 4: Problem statement:
This project addresses the issue of noise in audio signals, which diminishes quality and impacts the listening experience. The objective is to use filtering techniques to eliminate or minimize noise and improve the overall audio quality.

## Slide 5: Project Source:
The idea of the project is taken from the github account of alirezajaberirad[1].

## Slide 6: Tools Used:
MATLAB[2]: A software tool widely used for processing and analyzing discrete data, including signal processing applications and computational mathematics.
Fourier transform[3]: Used to decompose data represented as a function of time or space into frequency components.
fft function[4][5]: Implements a fast Fourier transform algorithm in MATLAB, reducing computational cost compared to other direct implementations.
conv and filter functions: Useful tools for modifying the amplitude or phase of input data using a transfer function.
Figure 1,
MATLAB Logo
6

## Slide 7: Methodology:
The project methodology comprises the following steps:
Figure 2, Flowchart of Program

## Slide 8: Step 1, Signal Analysis:
Read the noisy audio signal and extract its sampling frequency.
Apply the Fast Fourier Transform (FFT) to analyze the frequency content and phase information of the signal.
Visualize the magnitude spectrum and phase spectrum of the signal.

## Slide 9: Step 1, Signal Analysis (Cont.):
Code:
Figure 3.1, Signal Analysis Section Code

## Slide 10: Step 1, Signal Analysis (Cont.):
Output:

## Slide 11: Step 2, Filter Design:
Design an initial filter by specifying the filter coefficients.
Compute the frequency response of the initial filter using the ‘freqz’ function.
Plot the magnitude and phase spectra of the filter's frequency response.
Visualize the poles and zeros of the filter using the ‘fvtool’ function.

## Slide 12: Step 2, Filter Design (Cont.):
Code:
Figure 4, System Design Section Code

## Slide 13: Step 2, Filter Design (Cont.):
Output:
13

## Slide 14: Step 3, Impulse Response Calculation:
Calculate the impulse response of the initial filter using the ‘impz’ function.
Plot the impulse response to analyze its characteristics and determine its length.

## Slide 15: Step 3 Impulse Response Calculation (Cont.):
Code and Output:

## Slide 16: Step 4, Filtering Process:
Calculate the impulse response of the initial filter using the ‘impz’ function.
Plot the impulse response to analyze its characteristics and determine its length.

## Slide 17: Step 4, Filtering Process (Cont.):
Code:
Figure 7, Filtering Process Section Code

## Slide 18: Step 5, Results:
The project yielded the following results:
Frequency spectra and phase spectra of the original noisy audio signal.
Frequency response of the initial filter, including magnitude and phase spectra.
Impulse response of the initial and modified filters.
Filtered audio signals at different stages of filtering.

## Slide 19: Conclusion:
In conclusion, this project effectively utilized filtering techniques to reduce noise and enhance the audio quality of a noisy signal. The analysis of frequency spectra, filter characteristics, and impulse responses provided valuable insights, highlighting the significance of audio filtering techniques in improving audio signals.

## Slide 20: References:
Alirezajaberirad, Filtering Noisy Audio, https://github.com/alirezajaberirad/Signals-and-Systems/tree/main/CA2%20-%20Filtering%20Noisy%20Audio
MATLAB, https://www.mathworks.com/products/matlab.html
MathWorks, Fourier Analysis and Filtering, https://in.mathworks.com/help/matlab/fourier-analysis-and-filtering.html?s_tid=CRUX_lftnav
Fast Fourier Transform, https://en.wikipedia.org/wiki/Fast_Fourier_transform#:~:text=A%20fast%20Fourier%20transform%20(FFT,frequency%20domain%20and%20vice%20versa.
MathWorks, Fast Fourier Transform (FTT), https://in.mathworks.com/help/matlab/math/fourier-transforms.html

## Slide 21: THANK YOU